Physiotherapy Hi – Power laser module for FAVORITE – 3000 laser.

INSTRUCTIONS FOR USE

1. General Information

  - The Hi-Power laser module is developed as an interchangeable laser head for operation with Favorite 3000 laser therapy device. The Hi-Power laser module can be connected to the main electronic block instead of regular laser modules via electrical cable. The usage of Hi-Power module allows to receive faster therapeutic effect, to make the procedure shorter, and to irradiate bigger skin surface in distant or scanning modes.

  - For the use of Hi- Power module in a contact mode, special optical lens is designed to be screwed on the output end of the module. The glass lens can be easily cleaned with ethanol after the procedure.

  - The Hi-Power module is connected with the electronic block with a flexible spiral cable and screw-on connector. The output aperture of the module is equipped with a plastic Protective Cup that is put over the lens. The Protective Cup must be removed before carrying out the therapy procedure and put back on the module after transportation and storage.

2. Technical Specifications

| Output optical power, max. | 300 mW |
| --- | --- |
| Emitted wavelength, within the range | 810…..890 |
| Outer Diameter | 35 mm |
| Length | 125 mm |
| Weight, Netto | 80 g |
| Cable length | 1.5 m |

3. Safety Precautions

Phisiotherapy Laser module is a source of continuous invisible laser radiation and corresponds to  3 B class IEC 60601-2-22-95 (International Electro technical Commission) regulations.

It is prohibited to:

- Observe the laser radiation (beams) with unprotected eye;

- To bring in the reflective materials (mirrors, polished metal) in the beam/radiation zone;

- Operate by unauthorized personnel.